## Slide 1
MACHINE LEARNING PROJECT | GROUP 7
CONTEXTUAL BANDIT-BASED
ADAPTIVE SYNCHRONIZATION
AND RETRAINING OF UAV
NETWORK DIGITAL TWINS
Machine Learning-Based Adaptive Multi-UAV Coordination
N. Hasini — 2520040039
Ch. Sai Lahari — 2520040023
Guide: Mr. N. Lava Prasad, Assistant Professor, Department of ECE
Course: Machine Learning (25SC2107E) | A.Y. 2026–27
FINAL PROJECT PRESENTATION • SOFTWARE PROTOTYPE

## Slide 2
Project overview
What the prototype demonstrates—and what remains planned
MACHINE LEARNING PROJECT | GROUP 7
02
01 Problem
Different UAV distances and speeds cause arrival-time mismatch.
02 ML baseline
A Random Forest model explores required-speed prediction.
03 Synchronization
A three-UAV simulation compares arrival times before and after speed adjustment.
04 Context-aware idea
Traffic, load, cost and synchronization error are proposed as decision context.
05 Next stage
Train and validate a true online contextual-bandit policy and adaptive retraining loop.
Scope note: current evidence is from a software prototype and synthetic scenarios, not real-UAV flight trials.

## Slide 3
Background: UAV networks and digital twins
Why coordination and twin freshness matter
MACHINE LEARNING PROJECT | GROUP 7
03
• UAVs are used in communication, surveillance, disaster response, inspection and delivery.
• Each vehicle has its own position, speed, route, battery and communication conditions.
• A Digital Twin (DT) is a virtual representation used to monitor, estimate and reason about the physical system.
• The twin can become stale when the real network changes faster than it is updated.
• Updating too often may consume communication bandwidth, energy and computation; updating too slowly may reduce fidelity.

## Slide 4
Problem statement
Different starting distances and speeds create arrival-time mismatch
MACHINE LEARNING PROJECT | GROUP 7
04
Unequal travel distances
The UAVs start at different coordinates and travel toward one common target.
Unequal speeds
Different speed values create different estimated arrival times.
Changing context
Traffic, network load, latency and operational cost can change during a mission.
Core question: when should the system MOVE, WAIT/RETAIN, synchronize the twin, or RETRAIN a model?
A fixed policy may waste resources or react too slowly when conditions change.

## Slide 5
Objectives and scope
Prototype goals and boundaries
MACHINE LEARNING PROJECT | GROUP 7
05
• Simulate three UAVs moving toward a common target.
• Calculate distance, estimated arrival time and fleet arrival-time spread.
• Train a baseline Random Forest regressor on synthetic examples of required speed.
• Compare synchronization before and after applying predicted speeds.
• Define context features and illustrate MOVE / WAIT / RETRAIN decisions.
• Document limitations and a practical path toward an evaluated contextual-bandit system.

## Slide 6
Proposed system architecture
Target design: telemetry → prediction → context-aware decision → feedback
MACHINE LEARNING PROJECT | GROUP 7
06
UAV / telemetry
position, speed,
battery, link
State estimation
distance, ETA,
sync error
ML predictor
required speed /
confidence
Context builder
traffic, load,
cost, delay
Decision policy
MOVE / WAIT /
RETRAIN
Twin update & log
act, observe,
reassess
Feedback loop: compare predicted and observed state; monitor drift and synchronization error; update the policy only when justified.
Architecture is the intended workflow; not every block is fully implemented in the current prototype.

## Slide 7
End-to-end workflow
Six stages for the proposed adaptive system
MACHINE LEARNING PROJECT | GROUP 7
07
1. Collect state
Position, speed, target, network signals
2. Estimate ETA
Distance ÷ speed; compare fleet arrivals
3. Predict
Baseline ML estimates required speed
4. Build context
Traffic, load, cost, sync error, confidence
5. Choose action
Policy selects MOVE / WAIT / RETRAIN
6. Observe feedback
Measure outcome and reassess
The feedback loop is a design goal; a validated online learning loop remains future work.

## Slide 8
Simulation setup: three UAVs
Initial coordinates, common target and speeds
MACHINE LEARNING PROJECT | GROUP 7
08
Initial positions
UAV 1: (0, 0)
UAV 2: (0, 10)
UAV 3: (10, 0)
Motion parameters
Common target: (20, 20)
Initial speeds: 0.8, 0.5 and 1.0 m/s
Assumption: straight-line distance
U1
U2
U3
Target
The diagram is schematic, not a geographic map. Coordinates are in metres for the toy simulation; real flight dynamics and obstacles are not modelled.

## Slide 9
Distance and initial arrival-time calculation
Using straight-line distance and ETA = distance / speed
MACHINE LEARNING PROJECT | GROUP 7
09
Chart: Distance to target
| UAV 1 | UAV 2 | UAV 3
Distance (m) | 28.28 | 22.36 | 22.36
Chart: Initial estimated arrival times
| UAV 1 | UAV 2 | UAV 3
Initial ETA (s) | 35.36 | 44.72 | 22.36
Values are computed from the stated coordinates and initial speeds; they are not measured flight telemetry.

## Slide 10
Synchronization metric
Measure the gap between earliest and latest arrival
MACHINE LEARNING PROJECT | GROUP 7
10
Earliest arrival
min(t₁, t₂, t₃)
Latest arrival
max(t₁, t₂, t₃)
Arrival-time spread
max(tᵢ) − min(tᵢ)
Lower spread means closer arrival-time alignment in this simplified simulation.
Important: some slides in the source deck also use the label “synchronization error” for a different value. This presentation uses arrival-time spread for the directly interpretable seconds-based comparison.

## Slide 11
Machine-learning baseline
Random Forest regression on synthetic scenarios
MACHINE LEARNING PROJECT | GROUP 7
11
• Model: RandomForestRegressor with 100 trees.
• Training data: 1,000 synthetic scenarios.
• Features described in the prototype: distance, current speed, arrival time, common time and synchronization error.
• Target: required speed, generated from distance / common time and clipped to 0.2–2.0 m/s.
• Split: 800 training rows and 200 testing rows.
• The model learns a synthetic relationship; performance does not establish generalization to real UAV flight conditions.

## Slide 12
ML training and inference pipeline
From generated scenarios to predicted speed
MACHINE LEARNING PROJECT | GROUP 7
12
Generate
Create synthetic
state rows
Prepare
Select features
and target
Split
800 train /
200 test
Train
Random Forest
regressor
Evaluate
MAE and R²
Infer
Predict speed
for each UAV
Reproducibility note: because the target is derived from the same scenario features, high test scores can be expected and should not be interpreted as real-world flight accuracy.

## Slide 13
Reported synthetic-model evaluation
Metrics shown in the earlier project prototype
MACHINE LEARNING PROJECT | GROUP 7
13
MAE = 0.0294
Mean absolute error on the held-out synthetic test split.
R² = 0.9891
Coefficient of determination reported for the synthetic test split.
Interpretation: the model closely reproduces the synthetic target-generation rule under this setup.
These figures are inherited from the project’s reported run; regenerate the notebook to verify them before final submission.

## Slide 14
Predicted speed example
Prototype output used to adjust arrival-time alignment
MACHINE LEARNING PROJECT | GROUP 7
14
Chart: Predicted speeds
| UAV 1 | UAV 2 | UAV 3
Predicted speed (m/s) | 0.629 | 0.498 | 0.496
UAV 1
Distance 28.28 m
Predicted speed ≈ 0.629 m/s
UAV 2 / UAV 3
Predicted speeds ≈ 0.498 and 0.496 m/s
Illustrative software result

## Slide 15
Result: arrival-time alignment
Before and after predicted-speed adjustment
MACHINE LEARNING PROJECT | GROUP 7
15
Chart: Arrival times
| UAV 1 | UAV 2 | UAV 3
Before (s) | 35.36 | 44.72 | 22.36
After (s) | 44.97 | 44.87 | 45.09
Before adjustment
35.36 s, 44.72 s, 22.36 s
Spread ≈ 22.36 s
After adjustment
44.97 s, 44.87 s, 45.09 s
Spread ≈ 0.22 s
Large reduction in arrival-time spread in the simplified simulation.

## Slide 16
Contextual bandit: proposed decision layer
The decision depends on context and observed reward
MACHINE LEARNING PROJECT | GROUP 7
16
• A contextual bandit observes a context vector, selects an action, and receives feedback or reward.
• Possible context: traffic level, network load, communication delay, synchronization error, model confidence and operational cost.
• Candidate actions: MOVE, WAIT/RETAIN, synchronize/update the twin, or RETRAIN the prediction model.
• A reward could trade off synchronization quality against update frequency, latency, energy and computation.
• A genuine learning implementation needs a defined policy, reward observations, exploration strategy and evaluation over repeated episodes.
Current status: action logic is demonstrated illustratively; a validated trained online contextual-bandit policy remains future work.

## Slide 17
Context features and why they matter
Inputs proposed for the adaptive policy
MACHINE LEARNING PROJECT | GROUP 7
17
Traffic
Congestion or mission density can affect movement and communication.
Network load
High load may increase queueing and update delay.
Operational cost
Energy, bandwidth and computation should be considered.
Synchronization error
A larger arrival-time spread may call for correction.
Model confidence / drift
Low confidence or rising prediction error may justify validation or retraining.
These are proposed context variables; the current toy simulation does not provide real network measurements.

## Slide 18
Candidate actions: MOVE, WAIT/RETAIN, RETRAIN
Intended interpretation of each action
MACHINE LEARNING PROJECT | GROUP 7
18
MOVE
Continue or adjust UAV motion using a predicted speed, subject to safety and mission constraints.
WAIT / RETAIN
Temporarily hold the current action or retain the existing twin/model when immediate change is not justified.
RETRAIN
Trigger model update only after drift/quality checks and sufficient validated data are available.
Safety note: a real UAV system must enforce collision avoidance, geofencing, battery reserve, communications-loss handling and operator override independently of the learning policy.

## Slide 19
Adaptive reassessment loop
A conceptual response to changing conditions
MACHINE LEARNING PROJECT | GROUP 7
19
Observe
Collect new state and network context
Check
Compare prediction error and sync spread with thresholds
Decide
Select MOVE / WAIT / RETRAIN under constraints
Act
Apply safe action or keep the current state
Verify
Measure outcome; log reward and model performance
This is a design workflow, not evidence of a fully deployed real-time controller.

## Slide 20
Dataset strategy
Synthetic synchronization data and public flight telemetry
MACHINE LEARNING PROJECT | GROUP 7
20
Synthetic dataset used for baseline
1,000 generated scenarios; 800 training and 200 test samples. Target required speed is calculated from distance and common time.
Public telemetry dataset explored
Autonomous waypoint mission CSV includes time, position, altitude, velocity/speed and battery fields. It is not labelled for multi-UAV synchronization.
Source repository: https://github.com/yogesh031020/drone-flight-operations-data
Dataset limitation: a single-flight telemetry record cannot directly validate fleet arrival synchronization, bandit reward or retraining decisions without additional labels and carefully designed experiments.

## Slide 21
Public telemetry: fields and use
Potential use for exploratory analysis—not direct proof of fleet synchronization
MACHINE LEARNING PROJECT | GROUP 7
21
Field | Meaning | Possible analysis
time_s | Timestamp / elapsed time | Order samples; derive time intervals
lat, lon | Geographic position | Track route and estimate displacement
altitude_m | Altitude | Explore vertical profile
vx_ms, vy_ms, vz_ms | Velocity components | Derive or compare speed estimates
speed_ms | Speed magnitude | Baseline next-sample speed prediction
battery_pct | Battery percentage | Explore energy state / trend
Confirm the actual CSV headers, missing values and sampling interval in the notebook before reporting dataset statistics.

## Slide 22
Visualizations and evaluation plan
What should be plotted and measured
MACHINE LEARNING PROJECT | GROUP 7
22
Prediction quality
Actual vs predicted speed; residual plot; MAE and R².
Synchronization
Before/after arrival times; spread over time.
Policy behaviour
Action counts, cumulative reward and regret over episodes.
Twin freshness
Update frequency and prediction error / drift threshold.
Resource cost
Communication, energy and compute overhead, if measured.
Graphs without real measured values must be labelled as simulated or illustrative; do not present them as empirical results.

## Slide 23
Results summary
What the current prototype supports
MACHINE LEARNING PROJECT | GROUP 7
23
Working baseline
Random Forest regression and speed-prediction workflow.
Simulation
Three-UAV arrival-time calculations and comparison.
Reported metrics
Synthetic test MAE 0.0294; R² 0.9891.
Reported arrival-time spread: approximately 22.36 s before adjustment and 0.216 s after adjustment in the cited prototype run.
These results demonstrate feasibility of the toy synchronization calculation. They do not establish real-world safety, generalization or a trained contextual-bandit advantage.

## Slide 24
Limitations and risks
Current gaps that matter for evaluation
MACHINE LEARNING PROJECT | GROUP 7
24
• Three-UAV, straight-line simulation is a simplified model; no high-fidelity dynamics or obstacle avoidance.
• Synthetic target generation can make prediction metrics optimistic.
• Public single-flight telemetry does not itself provide fleet synchronization labels.
• Contextual-bandit policy and reward must be trained and evaluated across repeated episodes before claiming learned behaviour.
• Adaptive retraining needs drift detection, data validation, rollback and safety checks.
• No real UAV, hardware-in-the-loop or operational field validation is claimed.

## Slide 25
Future work and implementation roadmap
Steps to turn the prototype into a validated adaptive system
MACHINE LEARNING PROJECT | GROUP 7
25
1. Data
Use synchronized multi-UAV telemetry and document labels / sampling.
2. Baselines
Compare fixed policy, heuristic policy and ML-only synchronization.
3. Bandit
Implement a contextual policy with explicit action set and reward.
4. Evaluation
Run repeated scenarios; report reward, regret, sync spread and cost.
5. Retraining
Add drift checks, minimum-data rules, validation and rollback.
6. Safety
Add constraints, fault handling and simulation / hardware-in-loop tests
Success criterion: improved synchronization and twin freshness without unjustified update, energy or communication overhead.